## Slide 1: Compute Project Bill of Materials (B.O.M)
EAC-B01

## Slide 2: Bill of Materials, B.O.M. OVERVIEW
The purpose of this lesson is to provide you with the knowledge to estimate the material requirements for a vertical construction project.

## Slide 3: Learning Objectives TLO
Provided a vertical construction
mission,a scientific calculator, a
computer, software applications, and
references, compute a project bill of
materials to account for all Class IV
quantities per the references.
(1361-SRVY-2003)

## Slide 4: Learning Objectives ELO
(1). Provided written project specifications, design
drawings, a scientific calculator, blank material takeoff sheets,
and references, calculate concrete requirements per the FM
5-428. (1361-SRVY-2003a)
(2). Provided written project specifications, design
drawings, a scientific calculator, blank material takeoff sheets,
and references, calculate masonry requirements per the FM
5-428. (1361-SRVY-2003b)
(3). Provided written project specifications, design
drawings, a scientific calculator, blank material takeoff sheets,
and references, calculate lumber/plywood requirements per
the FM 5-426. (1361-SRVY-2003c)

## Slide 5: Learning Objectives ELO
(4). Provided written project specifications, design
drawings, a scientific calculator, blank material
takeoff sheets, and references, calculate finish
material requirements per the FM 5-426.
(1361-SRVY-2003d)
(5). Provided written project specifications, design
drawings, a scientific calculator, completed
lumber/plywood consolidations, blank material
estimate sheets, and references, estimate
construction hardware quantities per the FM 5-426.
(1361-SRVY-2003e)
(6). Provided written project specifications, design
drawings, a scientific calculator, completed material
takeoff sheets, and references, compile bill of
materials (BOM) per the FM 5-426.
(1361-SRVY-2003f)

## Slide 6: METHOD & MEDIA
Lecture
Demonstration
Practical Application
  Computer Slides
  Dry-erase Board

## Slide 7: EVALUATION
Performance Evaluation Exam

## Slide 8: SAFETY / CEASE TRAINING (CT) BRIEF
Fire
Tornado
Safety is Paramount

## Slide 9: QUESTIONS
?

## Slide 10: Principles of Estimating
Estimating is the calculation of the approximate amount of material and/or labor requirements to build a construction project.
Estimates are prepared from finished working drawings and project specifications.

## Slide 11: Qualifications:
Be able to read and scale drawings.
Posses a good working knowledge of math.
Be able to visualize the work required.
Working knowledge of construction methods and materials.
Knowledge and ability to assemble materials into working units.

## Slide 12: 2 Basic Calculations
Measurement:
  Descriptions of materials and items of work.
  Dimensions of items of work, and materials required.
  Calculating the quantities of materials, and items of work.
Pricing:
  Arithmetic used to determine the costs of items

## Slide 13: ?
Name some of the qualifications an estimator need to have in order to compile accurate estimates.
What are the two basic calculations involved in construction project estimations?
Notes: ANSWER: Able to read and scale drawings. Good knowledge of math. Mentally visualize work required. Knowledge of construction methods/materials.
ANSWER: Measurement and Pricing.

## Slide 14: Mathematical Equations
The application of basic
mathematical computations is all
that is necessary to compile
accurate project material and/or
labor requirements.
  Three basic conversions:
    Linear
    Area
    Volume

## Slide 15: Linear Conversion (Inches / Feet)
Conversions used to determine such
items of work such as: rafter, joist & stud
requirements.
Feet x 12 = inches
  3’ x 12 = 36”
Inches / 12 = Decimal feet
  36” ÷ 12 = 3’
Fractions:
  Numerator / denominator = Decimal parts of an inch.
    ¾”: 3 ÷ 4 = 0.75”
Decimals:
  Decimal parts of an inch / 12 = Decimal parts of a foot.
    0.75” ÷ 12 = .0625’

## Slide 16: LINEAR CONVERSION CALCULATION
DEMONSTRATION

## Slide 17: Area Conversion (Square Feet)
Conversion used to determine such items of work such as: plywood, paint, siding & concrete block requirements.
  Rectangles:
    Walls: L (ft) x H (ft) = Area (sqft/sf)
    Floors: L (ft) x W (ft) = Area (sqft/sf)
      10’ x 8’ = 80 sqft
  Triangles:
    Base (ft) x H (ft)
      2
      10’ x 10
  2
  Trapezoids:
    H (ft) x ½ the sum of the parallel sides = Area (sqft/sf)
      10’ x ((20 + 40) ÷ 2) = 300 sqft
= Area (sqft/sf)
= 25sqft

## Slide 18: AREA CONVERSION CALCULATION
DEMONSTRATION

## Slide 19: Volume Conversion (Cubic Feet & Cubic Yards)
Conversions used to determine such items as concrete, sand, aggregate & mortar.
  L (ft) x W (ft) x H (ft) = Volume (cuft/cf)
    10’ x 10’ x 8’ = 800 cuft
  Volume (cf) ÷ 27 = Volume (cuyd/cy)
    800 cf ÷ 27 = 29.63 cuyd
  Volume (cy) x 27 = Volume (cuft/cf)
    29.63 cy x 27 = 800 cuft

## Slide 20: VOLUME CONVERSION CALCULATION
DEMONSTRATION

## Slide 21: Perimeter Rule
A progressive calculation to compute areas and volumes.
Rectangular Shaped:
  Footing dimensions:
    Length: 32.67’
    Width: 16.67’
    Height: 0.67’
    Depth: 1.33’
  (Outside length (ft) + Inside width (ft) ) x 2 = Total perimeter length (ft)
    (32.67’ + 14.01’) x 2 = 93.36’
  Total perimeter length (ft) x H (ft) = Area (sqft/sf)
    93.36’ x 0.67’ = 62.55 sqft
  Area (sf) x D (ft) = Volume (cuft/ft)
    62.55 (sf) x 1.33’ = 83.19 cuft

## Slide 22: Perimeter Rule (Continued)
Irregular Shaped:
  Pentagon (5 sides)
    Footing Length (one side): 20.48’
    Height: 0.67’
    Depth: 1.33’
    Total outside perimeter length: 102.4’
    Total inside perimeter length: 95.75’
  (Outside Length (ft) + Inside Length (ft)) ÷ 2 = Total continuous perimeter length (ft)
    (102.4’ + 95.75’) ÷ 2 = 99.08’
  Total continuous perimeter length (ft) x H (ft) = Area (sqft/sf)
    97.58’ x 0.67’ = 66.38 sqft
  Area (sf) x D (ft) = Volume (cuft/cf)
    66.38 sqft x 1.33’ = 88.28 cuft

## Slide 23: PERIMETER RULE CALCULATION
DEMONSTRATION

## Slide 24: Standard Lumber Length Calculation
Used to determine the optimum length of lumber to minimize waste, when cutting specific small items of work.
Used for:
  Bridging
  Blocking
  Treads & Risers
  Headers
  Jack Studs
  etc…

## Slide 25: Standard Length Calculation (Part 1)
Length In Place (LIP) Measurement (in):
  Actual length of one piece of the small item of work
Quantity of LIP Requirements (ea):
  Counted off drawings or by calculation.
Convert Standard Lengths (in):
  Convert each standard length of lumber to inches.
8’ x 12” = 96” | 14’ x 12” = 168”
10’ x 12” = 120” | 16’ x 12” = 192”
12’ x 12” = 144” | 

## Slide 26: Standard Lumber Length Calculation (Part 2)
Number of LIP Pieces (ea): Number of LIP pieces that can be cut from each Standard Length of Lumber.
  Standard lumber length (in) ÷ LIP Measurement (in) = LIP pieces per standard lumber length. (Round Down)
    96” ÷ 21” = 4 Lip Pieces
Number of Standard Lengths (ea): How many Standard Lengths required to cut all LIP Pieces.
  Total LIP Requirements 4 Total LIP Pieces per Standard Lumber Length = Total Standard Lumber Lengths required. (Round Up)
    13 ÷ 4 = 4 8’ Lengths of Lumber

## Slide 27: Standard Length Calculation (Part 3)
Standard Length to Use (ea) to minimize waste.
  Standard Lumber Length x Number of LIP Pieces which can be cut from that length = Total Linear feet of Standard Lumber Length.
    8’ x 4 = 32’
  Compare each value. The lowest value will identify the Standard Lumber Length with the minimal amount of waste.

## Slide 28: Standard Lumber Length Calculation Example
13 pieces of floor bridging, 1’-9” long are needed to stiffen the floor joists.
8’ x 12” = 96” | 96” ÷ 21” = 4 | 13 ÷ 4 = 4 | 8’ x 4 = 32’
10’ x 12” = 120” | 120” ÷ 21” = 5 | 13 ÷ 5 = 3 | 10’ x 3 = 30’
12’ x 12” = 144” | 144” ÷ 21” = 6 | 13 ÷ 6 = 3 | 12’ x 3 = 36’
14’ x 12” = 168” | 168” ÷ 21” = 8 | 13 ÷ 8 = 2 | 14’ x 2 = 28’
16’ x 12” = 192” | 192” ÷ 21” = 9 | 13 ÷ 9 = 2 | 16’ x 2 = 32’
Converted
Standard
Length
LIP pcs cut
from std lgth
Number
of std lgth
Standard
lgth to use
Round
Round

## Slide 29
BREAK

## Slide 30
PRACTICAL APPLICATION
Math Review

## Slide 31: ?
Why would you want to select the lowest value of your LIP calculations off of the standard lumber length?
What are the three fundamental conversion formulas that are used to estimate material requirements?
Notes: ANSWER: Because the least value is related to the least amount of waste.
ANSWER: Linear, area, and volume conversions.

## Slide 32: Material Takeoff List (MTO)
MTO: Lists all items of work, detailing:
  Dimensions
  Quantities of work
  Units of measure conversions
Rules for Compiling:
  Study all drawings, notes & specifications.
  Measure everything as shown.
  Measure everything you can see.

## Slide 33: Time Savers
Never use long words if short ones will do.
Use abbreviations.
Keep all dimensions, figures and notes.
Always start in the same place on each drawing.
Highlight / mark-off items, notes and specifications when completed.
Take advantage of duplication of design.

## Slide 34: MTO - PRECEDENCE
If a work item is different, list it separately on the MTO. The items of work are estimated in a logical sequence using the following order of precedence:
  1st – EXCAVATION
  2nd – CONCRETE
  3rd – MASONRY
  4th – LUMBER
  5th – FINISH MATERIALS

## Slide 35: Concrete & Masonry MTO Estimating Sequence
Excavation: cuyd/cy
  Calculate amount by using the dimension measurements for the outside face of the footings ≠ dimensions of the outside face of the walls.
Concrete:
  Ready-Mix cuft/cf
  Batch Mix cuft/cf
  Reinforcement Bar ft
  Wire Mesh sqft/sf
  Poly Vapor Barrier sqft/sf
  Expansion Joint Filler ft
  Base Course cuft/cf
Masonry Wall Surface sqft/sf
  Vertical Reinforcement ft
  Horizontal Reinforcement ft

## Slide 36: Lumber MTO List
Lumber is taken off the notes drawings and specifications as:
  Lumber as the number of standard lumber lengths.
  Plywood & Siding by the square footage to be covered.
  Finish Trim by the linear foot.
Two Categories for Lumber MTO:
  Rough Carpentry
    Floor Framing (lumber & plywood)
    Wall Framing (lumber & plywood)
    Roof Framing (lumber & plywood)
    Wooden Forms (lumber & plywood)
  Finish Carpentry
    Siding
    Trim Work

## Slide 37: Finish Material MTO List
Finish materials are items required to “finish” the exterior and interior of a structure:
  Doors & Windows ea
  Shingles sqft/sf
  Drywall sqft/sf
  Paint sqft/sf
  Insulation sqft/sf

## Slide 38: MATERIALS TAKEOFF LIST
DEMONSTRATION

## Slide 39: MTO Demo Foundation Plan

## Slide 40: MTO Demo Foundation Details

## Slide 41: MTO Demo Foundation & Floor Section

## Slide 42
Concrete and Masonry Material Takeoff Sheet |  |  |  | 
Item of Work | Dimensions | Quantity Required | Concrete Volume (L x W x H) | Masonry Area (L x H)
Project: | Total Volume of Concrete = |  | cf | 
Estimator: | Total Surface Area of Masonry Units = |  |  | sf

## Slide 43: MTO Demo Floor Framing Plan

## Slide 44
Lumber Material Takeoff Sheet |  |  |  |  |  |  |  |  |  | 
Descriptive Item of Work |  | Item U/M | LIP Measure |  | LIP Qty | STD Lgth to Use |  | STD Lgth Qty |  | LIP PCS/ STD Lgth
Bridging Calculation: LIP |  |  |  |  |  |  |  |  |  | 
Converted Standard Length | LIP pieces cut from std lgth |  |  | Number of std lgth |  |  | Standard lgth to use |  |  | 
8' x 12" = 96" |  |  |  |  |  |  |  |  |  | 
10' x 12" = 120" |  |  |  |  |  |  |  |  |  | 
12' x 12" = 144" |  |  |  |  |  |  |  |  |  | 
14' x 12" = 168" |  |  |  |  |  |  |  |  |  | 
16' x 12" = 192" |  |  |  |  |  |  |  |  |  | 
Project: |  |  |  |  |  |  |  | Date: |  | 
Estimator: |  |  |  |  |  |  |  | Sheet of |  | 

## Slide 45
BREAK

## Slide 46
PRACTICAL APPLICATION
Part #1 Material Takeoff Sheets

## Slide 47: ?
What is a materials takeoff sheet used for?
Where does the information come from to create a MTO?
Notes: ANSWER: The MTO is a listing of all items of work, dimensions (sizes), quantities of work, and units of measure conversions.
ANSWER: It is extracted from project specifications and working drawings.

## Slide 48
BREAK

## Slide 49: Material Estimate Sheet (MES)
MES puts the information on the MTO into detail, showing:
  Description of work.
  Detailed description of materials.
  Units of measure of materials.
  Quantities of “dissimilar” materials.
  Quantities of “like” materials.
  Waste factor allowances.
  Total material quantities, including waste.

## Slide 50: MES (Ready-Mix Concrete)
Ready-mix Concrete volumes from the MTO are converted and rounded up to the nearest whole cuyd.
  The appropriate waste factor is calculated and added, after the concrete volume is converted to cuyds.

## Slide 51: MES (Batch Mix Concrete)
Batch mix concrete is a proportional mix of:
  Portland Cement
  Sand
  Aggregate (Gravel)
    Water (not figured into the estimate)
Standard mix ratio (1:2:3) of:
  (1) part Portland Cement
  (2) parts Sand
  (3) parts Aggregate (Gravel)
    A 1:2:3 mix concrete will achieve a compressive strength of 2000 psi at 28 days.

## Slide 52: Batch Mix Concrete Estimating Calculation
Total concrete volume from MTO x 1.5 (3/2 rule) = Concrete Proportion Ratio (CPR)
  92.98 cy x 1.5 = 139.47
Multiply CPR to mix ratio.
  (1/6 x CPR) + Waste Factor = Total bags of Portland Cement. (Round up)
    1/6 x 139.47 = 23.25 + 5% = 25.0 bg
  ((2/6 x CPR) ÷ 27) + Waste Factor = Total cuyds of Sand
    (Round up to nearest half cubic yard)
    ((2/6 x 139.47) ÷ 27 = 1.72 + 10% = 2.0 cy
  ((3/6 x CPR) ÷ 27) + Waste Factor = Total cuyds of Aggregate
    (Round up to the whole cubic yard)
    ((3/6 x 139.47) ÷ 27 = 2.58 + 10% = 3.0 cy

## Slide 53: MES Concrete Masonry Units (CMU)
Nominal Dimensions:
  16” x 8” x 8”
Actual Dimensions
  15 5/8” x 7 5/8” x 7 5/8”
    3/8” mortar joint between blocks.
Estimate CMU by Square Feet
One concrete block = 0.89 sqft of surface area.

## Slide 54: CMU Estimating Calculation
Total masonry surface area from MTO (sf) ÷ 0.89 (sf) = Number of CMU blocks (ea)
  325.02 ÷ 0.89 = 365.19
Number of CMU + Waste Factor = Total CMU blocks (ea) (Round up to nearest whole block)
  365.19 + 2% = 373.0 blocks

## Slide 55: MES (Mortar)
Mortar is a proportional mix of:
  Portland Cement
  Masonry Cement
  Sand
    Water (not figured into the estimate)
Standard mix ratio (1:1:6) of:
  (1) part Portland Cement
  (1) parts Masonry Cement
  (6) parts Sand
    A 1:1:6 mix concrete will achieve a compressive strength of 2000 psi at 28 days.
    Bonded by a 3/8” mortar joint, bonding 0.054 cuft of block area.

## Slide 56: Mortar Estimating Calculations
Total number of blocks from MTO x 0.054 (cf) = Total amount of mortar to bond all blocks (cf)
  373 x 0.054 = 20.14
Multiply total mortar requirement to mix ratio.
  (1/8 x total mortar) + Waste Factor = Total bags of Portland Cement. (Round up)
    1/8 x 20.14 = 2.52 + 5% = 3.0 bg
  (1/8 x total mortar) + Waste Factor = Total bags of Masonry Cement. (Round up)
    1/8 x 20.14 = 2.52 + 5% = 3.0 bg
  ((6/8 x total mortar) ÷ 27) + Waste Factor = Total cuyds of Sand (Round up to the nearest half cubic yard)
    (6/8 x 20.14) ÷ 27 = 0.56 + 10% = 1.0 cy

## Slide 57: MES (Boards, Lumber, Timber & Plywood)
The unit of measure to estimate boards, lumber, and timber is board feet (bf).
  One board foot is equal to a piece of wood having 12 square inches of end area, and is 1 foot long.
The unit of measure to estimate plywood is sheet (sh).
  One sheet of plywood has 32 square feet of surface area.

## Slide 58: Boards, Lumber & Timber Estimating Calculations
Consolidate and total all “like” wood sizes & grades. Calculate board feet.
Total all “dissimilar” wood sizes & grades. Calculate board feet.
Board Feet Calculation
  ((Thickness (in) x Width (in) x Length (ft) x Quantity) ÷ 12) + Waste Factor = Total Board Feet (Round up)
(2” x 6” x 16’ x 6) ÷ 12 = 96.0 bf + 10% = 106.0 bf

## Slide 59: Plywood Estimating Calculation
Consolidate and total all “like” plywood sizes & grades. Calculate sheets required.
Total all “dissimilar” plywood sizes & grades. Calculate sheets required.
Sheet Calculation
  Total Surface area to be covered from MTO ÷ 32 (sf) = Total sheets required + waste factor = Total sheets to order. (Round up)
512 sqft ÷ 32 sqft = 1 6.0 sh + 15% = 19.0 sh

## Slide 60: MES (Nails) & Nail Estimating Calculations
Unit of measure for nails by the pound (lb).
Three formulas, based on nail size, are used to determine nail requirements.
  2d to 12d Nails:
    ((Nail size x Total bf of lumber to be fastened) ÷ 400) + Waste Factor = Total nails (lbs) (Round up)
(10d x 523 bf) ÷ 400 = 13.08 + 10% =
15.0 lbs

## Slide 61: Nail Estimating Calculations (cont)
  12d to 60d Nails:
    ((Nail size x Total bf of lumber to be fastened) ÷ 600) + Waste Factor = Total nails (lbs) (Round up)
(763 bf x 16d) ÷ 600 = 20.35 + 10% =
23.0 lbs
  2d to 12d Nails for plywood:
    ((32 sqft x Total sheets to be fastened) ÷ 400) + Waste Factor = Total nails (lbs) (Round up)
(32 sf x 19 sh) ÷ 400 = 1.52 + 10% =
2.0 lbs

## Slide 62
Material Estimate Sheet |  |  |  |  | 
Work Description | Detailed Material Description | Material U/I | Material Quantity | Waste Factor | Total Qty
Project: |  |  |  | Date: | 
Estimator: |  |  |  | Sheet of | 

## Slide 63: MATERIALS ESTIMATION SHEET (Mes)
DEMONSTRATION

## Slide 64
BREAK

## Slide 65
PRACTICAL APPLICATION
Part #1 & #2 Material Estimate Sheets

## Slide 66: ?
What is the purpose of a materials estimate sheet?
What is a “board foot”?
Notes: ANSWER: Materials estimates put the information contained in the material takeoff lists into a more detailed form.
ANSWER: A board foot is a piece of wood having an end area of 12 square inches, and a length of 1 foot.

## Slide 67
BREAK

## Slide 68: Bill Of Materials (BOM)
Consolidated list of:
  All material descriptions
  Quantities
  NSN’s
  Unit of issue
  Unit cost
  Total cost of individual items
  Total cost of all materials required
Source document used to order project materials.
Manufacturers, venders, companies and acceptable replacement items are also listed to prevent poor substitutions.

## Slide 69: Bill Of Materials (BOM)
STANDARD UNITS OF MEASURE |  |  |  | 
MATERIAL | U/M |  | MATERIAL | U/M
CONCRETE (Ready Mix) | cuyd |  | DIMENSION LUMBER | bf
SAND | 1/2 cuyd |  | TIMBER | bf
GRAVEL | 1/2 cuyd |  | PLYWOOD | sh
CEMENT | bg |  | TRUSS'S | ea
CONCRETE BLOCK | ea |  | DRYWALL | sh
REINFORCEMENT BAR | ft |  | NAILS | lb
WELDED WIRE | ro |  | SCREWS | bx
CRUSHED ROCK | cuyd |  | ANCHOR BOLTS | ea
POLY VAPOR BARRIER | ro |  | BOLTS | ea
FILL DIRT | cuyd |  | DRYWALL SCREWS | bx
BATT INSULATION | ro |  | DRYWALL TAPE | ro
PAINT | ga |  | DRYWALL COMPOUND | ga
HINGES | ea |  | LAP SIDING | sq
INSECT SCREEN | ro |  | T-111 SIDING | sh
ROOFING FELT | ro |  | CORRUGATED ROOFING | sh
ROLL ROOFING | ro |  | ASPHALT SHINGLES | sq
DOORS | ea |  | WINDOWS | ea
ELECTRICAL WIRE | ft |  | ELECTRICAL OUTLETS | ea
ELECTRICAL SWITCHES | ea |  | LIGHTING | ea
ELECTRICAL CONDUIT | ft |  | JUNCTION BOXES | ea
SERVICE HEAD | ea |  | CONDUIT CONNECTORS | ea
PLUMBING FIXTURES | ea |  | PLUMBING PIPE | ft
PIPE COUPLINGS | ea |  | FORM TIE WIRE | ft

## Slide 70
Bill of Materials |  |  |  |  |  | 
Detailed Nomenclature Description | NSN | U/I | Unit Cost | Qty Req | Total Cost | Source/ Substitute
Project: |  | Total Project Material Cost: |  |  |  | 
Estimator: |  | Date: |  |  | Sheet of | 

## Slide 71: ?
What is a bill of materials?
What is a bill of materials used for?
Notes: ANSWER: A bill of materials is an detailed listing of all material descriptions, quantities, NSN's, units of issue, unit costs, total cost of the item, and the total cost of all the materials required for the project.
ANSWER: It is the source document which is used to procure all required project materials.

## Slide 72: summary
MATHEMATICAL CONVERSIONS
MATERIAL TAKEOFF LISTS
MATERIAL ESTIMATION SHEET
BILL OF MATERIALS